## Slide 1
Project presentation
project title: Smart Air Quality Monitoring System

## Slide 2
Introduction
- Overview: The Smart Air Quality Monitoring System is designed to continuously track and analyze air quality in real-time. It utilizes multiple sensors to detect pollutants and environmental conditions, providing users with vital information about the air they breathe.
- Importance:
Health Impacts: Poor air quality is linked to respiratory issues, cardiovascular diseases, and overall reduced quality of life. According to the World Health Organization, air pollution causes millions of premature deaths annually.
- Environmental Effects: Air pollution contributes to climate change, harming ecosystems and biodiversity.
- Urbanization: With increasing urbanization, the demand for effective air quality monitoring is higher than ever. Cities often experience higher pollution levels due to traffic, industrial activities, and construction.

## Slide 3
the goal of the project
- Empower users with actionable insights regarding their air quality.
- Facilitate informed decisions about health and activities, particularly for sensitive groups (children, elderly, people with pre-existing conditions).

## Slide 4
hardware components
- MQ-135 Gas Sensor
- Functionality: Designed to detect a wide range of harmful gases, including ammonia (NH3), benzene, carbon dioxide (CO2), and other volatile organic compounds (VOCs).
- Working Principle: The sensor utilizes a metal oxide (MOX) layer that changes resistance in the presence of these gases, which is then converted to a voltage signal.
- Sensitivity Range: Effective in environments with gas concentrations from 10 to 1000 ppm, making it suitable for indoor air quality monitoring.

## Slide 5
hardware components
- *Dust Sensor (e.g., GP2Y1010AU0F)*
- *Functionality:* Measures particulate matter in the air, specifically PM2.5 and PM10, which are critical for assessing air quality.
- *Working Principle:* Uses an infrared LED and a phototransistor; when dust particles pass through the light beam, they scatter light, which the phototransistor detects and converts into an electrical signal.
- *Measurement Range:* Typically measures concentrations in micrograms per cubic meter (µg/m³), allowing for effective monitoring of air quality.
- Dust Sensor (e.g., GP2Y1010AU0F)
- Functionality: Measures particulate matter in the air, specifically PM2.5 and PM10, which are critical for assessing air quality.
- Working Principle: Uses an infrared LED and a phototransistor; when dust particles pass through the light beam, they scatter light, which the phototransistor detects and converts into an electrical signal.
- Measurement Range: Typically measures concentrations in micrograms per cubic meter (µg/m³), allowing for effective monitoring of air quality.

## Slide 6
hardware components
- DHT22 Sensor (Temperature and Humidity Sensor)
- Functionality: Measures ambient temperature and relative humidity, which are important factors influencing air quality and comfort.
- Working Principle: It uses a thermistor for temperature and a capacitive humidity sensor, providing digital output for accurate readings.
- Range:
- Temperature: -40 to +125 °C with ±0.5 °C accuracy.
- Humidity: 0 to 100% RH with ±2-5% accuracy.

## Slide 7
hardware components
Keypad Component
- Overview:
- The keypad serves as a user interface for the Smart Air Quality Monitoring System, allowing users to interact with the device, input commands, and view settings.
- Type of Keypad:
- Matrix Keypad: Typically a 4x4 matrix keypad, consisting of 16 keys, which allows for efficient input without requiring a lot of GPIO pins.
- Functionality:
- User Input: Enables users to set parameters, such as thresholds for air quality alerts or to navigate through different display screens (e.g., current air quality readings, historical data).
- Control Functions: Users can start or stop the air purifier/fan directly from the keypad, providing convenient control over the system.

## Slide 8
hardware components
Fan Component
- Overview:
- The fan is a vital part of the Smart Air Quality Monitoring System, used to enhance indoor air quality by circulating and filtering air when pollutant levels rise.
- Functionality:
- Air Circulation: The fan helps to distribute fresh air and reduce the concentration of indoor pollutants, improving overall air quality.
- Response to Air Quality: It activates automatically when air quality sensors detect high levels of harmful gases or particulate matter, providing immediate relief.

## Slide 9
circuit connections
- MQ-135 Gas Sensor:
- VCC Pin: Connect to 5V power supply from the ESP32.
- GND Pin: Connect to ground (GND).
- Analog Output Pin: Connect to MQ135_PIN (GPIO 34) on the ESP32. This pin reads the voltage output to determine gas concentrations.
- Dust Sensor (e.g., GP2Y1010AU0F):
- VCC Pin: Connect to 5V power supply.
- GND Pin: Connect to ground (GND).
- Analog Output Pin: Connect to DUST_READING_PIN (GPIO 35). This pin receives the analog signal corresponding to dust concentration.

## Slide 10
circuit connections
- DHT22 Sensor:
- VCC Pin: Connect to 5V power supply from the ESP32.
- GND Pin: Connect to ground (GND).
- Data Pin: Connect to DHT_PIN (GPIO 14). This pin is used for digital communication to retrieve temperature and humidity data.
- FAN Control:
- Control Pin: Connect to FAN_PIN (GPIO 13). This pin controls the fan operation based on the air quality data (e.g., turning on/off when pollution levels exceed a certain threshold).
- Relay Module (if used): If controlling a higher voltage fan, include a relay module connected to the ESP32. Connect the relay’s control pin to GPIO 13.

## Slide 11
circuit connections
- Keypad Connections (if applicable):
- Row Pins: Connect to GPIO pins (32, 33, 25, 26). These are used for scanning input from the keypad.
- Column Pins: Connect to GPIO pins (5, 18, 19, 23). These allow for detecting which key is pressed.

## Slide 12
Data Processing
- Overview:
- Data processing is a critical part of the Smart Air Quality Monitoring System. The ESP32 microcontroller collects data from various sensors, processes it in real-time, and takes actions like activating the fan or sending alerts. The system analyzes air quality parameters such as gas concentrations, particulate matter, temperature, and humidity to provide meaningful insights.
- Data Flow:
1. Sensor Data Acquisition:
- The MQ-135, Dust Sensor, and DHT22 continuously send raw sensor data (gas concentration, dust particles, temperature, and humidity) to the ESP32.
2. Analog to Digital Conversion:
- For analog sensors like the MQ-135 and Dust Sensor, the ESP32 reads the analog voltage from the sensors and converts it to digital values using its built-in ADC (Analog-to-Digital Converter). These values represent the levels of gases and particulate matter in the air.

## Slide 13
data processing
- Processing Logic:
- Thresholds for Air Quality:
- Predefined thresholds for acceptable air quality levels are set for each sensor. For example:
- MQ-135 Gas Sensor: A specific concentration of harmful gases (measured in ppm) may trigger an alert or the activation of the fan.
- Dust Sensor (PM2.5/PM10): If particulate matter readings exceed a safe limit (e.g., 50 µg/m³), the system activates the fan to improve air quality.
- Temperature and Humidity: The system can account for high temperatures or humidity, which may exacerbate poor air quality and trigger fan activation or alert notifications.
- *Alert Mechanism:*
- The ESP32 continuously compares the sensor data against the thresholds. When a sensor reading exceeds its limit, the system can trigger:
- Fan Activation: The fan turns on automatically to circulate and clean the air.
- Remote Notifications: The ESP32 can send data to a remote server, mobile app, or user via email or SMS, providing real-time updates.

## Slide 14
conclusion
- Summary of Accomplishments:
- The Smart Air Quality Monitoring System successfully integrates various sensors (MQ-135, Dust Sensor, DHT22) with the ESP32 microcontroller to monitor indoor air quality in real-time. It collects essential data on harmful gases, particulate matter, temperature, and humidity and responds automatically by controlling a fan to improve air quality when necessary.
- User Interface: The inclusion of a keypad allows users to interact with the system, customize settings, and manually control the fan. The system also logs data for remote monitoring, offering a convenient way to track air quality trends over time.
- Efficient Response: The system demonstrates its effectiveness in identifying poor air quality and responding by activating a fan to mitigate harmful conditions. This ensures a safer and healthier indoor environment.
- Real-world Impact:
- This system can significantly improve indoor air quality by empowering users to monitor pollution in real time. By addressing issues such as gas emissions and particulate matter, it can help reduce health risks related to respiratory and cardiovascular diseases.
- The project can also contribute to better air quality awareness, encouraging individuals to take preventive measures in areas with poor ventilation or high pollution levels.

## Slide 15
Thank you very much!